## Slide 1: GNU Radio Block Creation
Igor Povarich

## Slide 2: Goals
Create 2 GNURadio blocks
  Transmitter block
    Preamble (fixed)
    Flow ID (user configurable)
    User Data (user configurable)
    Checksum (calculation)
  Receiver block
    Catch the preamble to identify the start of the data stream
    Filter based on the flow ID
    Check for errors using the checksum
    Pass user data, if validated

## Slide 3: Transmitter Block
Functioning transmitter block that has been tested writing a packed byte stream
Encodes Preamble for simple identification (0x37 and 0x89)
Encodes Flow ID for filtering and payload size for parsing the user data
Calculates and encodes a simple 8-bit checksum for error identification
  The value 152 was used for the modulo calculation to avoid overflows because that seemed to be the max value a C++ char could encode
Packed Packet Framer File Sink output

## Slide 4: Receiver block
Performs the functions of the transmitter block in reverse
Since data from GNURadio Modulator blocks comes out as individual bits
Speculatively builds 2 8-bit bytes (16 bits) to look for the preamble
  Checked as matched strings
  If the assembled bytes don’t match the preamble, it steps back 15 steps (+1 from starting point)
Most data is reconstructed one bit a time, then packed into a bitset for processing

## Slide 5: Receiver block
If preamble AND flow id are matched, the valid_stream bool is set to true
  If flow id is not validated, it returns to trying to find the next preamble
Next, payload_size, user data, and checksum are extracted
The checksum is calculated from the extracted data and matched against the extracted checksum
  If they don’t match a warning is sent to the console
For a valid stream, all relevant data is passed through to the output

## Slide 6: Test flowgraphs
Two main GNURadio Companion graphs are used for testing
The first passes the pkt_framer output through a PSK Mod/Demod block combo to a file sink
The 2nd receives the data from the file sink

## Slide 7: testing
Main console output from the pkt_receiver block includes notifications about matching and user data
If the flow_id is mismatched, everything after the preamble match is skipped

## Slide 8: Challenges and Learning
Had a lot of difficulty with the exit conditions for the blocks in GRC (behavior when attempting to stop the simulation)
  Made testing more difficult and time-consuming
  Reason why I opted to have two separate graphs with a file sink in-between
Learned a lot about working with low-level binary data in GNURadio OOT blocks, especially how packing affects the way a data stream is processed or encoded
Re-learned some of the data type operations in C++
Like everyone else, I was confused by the single-bit output from the modulator blocks